## Slide 1: ECE 2140 SOC Design Convolution Neural Network on FPGA Theta
Thibaut Lanois: THL26@pitt.edu
Wen Wen: WEW55@pitt.edu
Pan Jieming: JIP40@pitt.edu
1 min

## Slide 2: A Typical Convolutional Neural Network (LeNet-5)
LeNet-5: Y. LeCun, L. Bottou, Y. Bengio, and P. Haffner. Gradient-based learning applied to document recognition. Proceedings of the IEEE, november 1998.
Convolutional Operation

## Slide 3: CNN SoC System Architecture Overview
Convolution layer
Fully connected layer
FIFO + Pooling layer
Controller
Router
Convolutional layers account for over 90% computation
FPGA has inherent parallelism
3 min

## Slide 4: Schedule and Status
Accomplishments last week:
  For given input image from CPU, Convolution/Pooling layer work as expected
  For router/controller/convo/pooling/BRAM, Individual/Integrated Test Benches design, synthesis, integration done
  Fully connected layer is in-progress
Working on this week:
  AXI bus for communication between CPU and FPGA
  Performance boosting with constraints
Challenges/ Difficulties / Needs in Integration Testing
  Floating-point to (16-bit) fixed-point data conversion
  Data/weight address calculation
2 min

## Slide 5: Fully connected layer (Optional Feature)
Function:
  Softmax:
    Preloading a BRAM with 512 fixed-point exponential values.
    Another BRAM is used to store the exponential of the output of the convolution for Softmax calculation later.
    A register is used to accumulate the sum of all outputs for Softmax.
  ReLU
  Selection between ReLu and SoftMax function
2 min

## Slide 6
Fully connected layer (Optional Feature)
280++ lines of code
ReLu
Preload Exponential LUT
Exponential conversion
2 min

## Slide 7: Convolution layer - overview
Function: To accelerate the computation of convolution of the kernels over the feature map with FPGA resources.
2 min
Difficulties
  Timing of control signals
  Fixed-point multiplication
  Precision degradation
Solution
  Controls go through the pipeline
  Using DSP IP from Xilinx
  1) Using 32 bit as output of the multiplier and then shifting data width downto 16 bit again, 2) Checking possible data overflow in shrinked 16 bit data with 32 bit outputs.

## Slide 8: Convolution layer - simulation
Testing through Integer and then Fixed point
  Next_output is registered through the pipeline.
  When Next_output is equal to 1, bias is added and accumulation starts.
  Bit shift happens at the output of multiplication.

## Slide 9: Convolution layer - synthesis
Final synthesis of the convolution block
Utilization
DSPs used in Convolution module

## Slide 10: Router | controller - overview
Function: to propagate the flow of data through the Pipelined Execution (Convolution and pooling)
2 min
Difficulties
  Timing of control signals
  Data addressing at the end of the rows
  Data addressing at the end of the feature maps
Solution
  Mealy FSM
  Did simulation a lot of time until addresses and data meet the expected ones ...

## Slide 11: Router | controller - simulation
Testing through 2 output data every cycle and the corresponding weight

## Slide 12: Router | controller - synthesis
Final synthesis of the router and controller blocks
Utilization
Route for calculating data address jumping to
new row

## Slide 13: FIFO | Pooling Layer - overview/simulation
Function: enable the parallelism and serializing feature maps from PEs (Processing Element) which conduct convolutional operations.
Testing through 2 input data every a few cycles and waiting for 4 data and then obtaining the maximum one
2 min
Integer
Fixed-point & negative

## Slide 14: FIFO | Pooling Layer - synthesis
Final synthesis of the fifo and pooling blocks
Utilization
Schematics screenshots
FIFO | Pooling
Overview

## Slide 15: Requirement Traceability Matrix
We’ve followed the RTM to test/debug our hardware system as the table below.
The test cases on the right of the red line are completed, and the left ones are in-progress.

## Slide 16: Final Testing waveform
Integration of controller/router/convolution/pooling modules works as expected.
Input from CPU
Output from Convolutional Layer
Output from Pooling Layer

## Slide 17: Final testing files
We compared the immediate data after pooling layer between C codes and hardware design as table below.
For obtaining one single output, 4x5x5x6=600 multiply-add calculations accumulate errors.
Within average error rate of ~ 0.0243, the results can be considered as acceptable.
16-bit Fixed-point in FPGA |  | 32-bit Floating-point in C |  | Absolute Error | Relative Error (%)
HEX | REAL | HEX | REAL | Avg: 0.0191 | 
1011 | 1.015 | 1066 | 1.025 | 0.0100 | 0.9756
FFF2 | -0.002 | 0047 | 0.017 | 0.0190 | 111.7647
FA0B | -0.375 | FA7A | -0.345 | 0.0300 | 8.6957
03C8 | 0.230 | 0426 | 0.259 | 0.0290 | 11.1969
FD42 | -0.130 | FD97 | -0.150 | 0.0200 | 13.3333
E810 | -1.484 | E864 | -1.475 | 0.0090 | 0.6102
FA36 | -0.325 | FA9F | -0.333 | 0.0080 | 2.4024
E6F0 | -1.510 | E763 | -1.538 | 0.0280 | 1.8205

## Slide 18: <CNN on FPGA theta> Summary
5 min
Accomplishments last week:
  For given input image from CPU, Convolution/Pooling layer work as expected
  For router/controller/convo/pooling/BRAM, Individual/Integrated Test Benches design, synthesis, integration done
  Fully connected layer is in-progress
Working on this week:
  AXI bus for communication between CPU and FPGA
  Performance boosting with constraints
Challenges/ Difficulties / Needs in Integration Testing
  Floating-point to (16-bit) fixed-point data conversion
  Data/weight address calculation